EXCRETA MANAGEMENT ASSESSMENT TOOL

# This assessment tool has been designed to assist UNHCR and WASH actors collect data on excreta management during a needs assessment. The main purpose of this tool is to identify problems related to excreta management and identify actions to bring conditions to UNHCR standards.

# This tool attempts to capture most of the common problems encountered with excreta management, however the user should apply common sense and document any additional problems that may not be covered.

# It is good practice to discuss the results of this assessment with members of the displaced community before departing. Matters of extreme urgency should be addressed immediately.

| EXCRETA MANAGEMENT INFRASTRUCTURE ASSESSMENT TOOL |
| --- |
| Assessor(s): ___________________________ ___________________________ | Contact details: ___________________________________ Date of assessment : ______/_______________/_______ |
| Site information Site location (District, Town, Village etc.): _____________________________ GPS Long: ______°_______ʹ_______ʺ GPS Lat: ______°_______ʹ_______ʺ  Planned camp  Unplanned camp  Urban collective centre  Host families  Rented accommodation  Public buildings  Other _________ Contact person: ______________________ Position: ____________________ | Number of men: _______ Number of women: _____ Number of children: _____ Phone number: _______ |
| Toilet coverage information ( Number of cubicles _______ ( Total daily users ________ ( Coverage rate ________(persons/toilet) ( Estimated % of population defecating in the open _______ |
| Privacy structure type ( Wood frame / plastic sheeting ( Wood frame / corrugated iron sheeting ( Wood frame / grass covering ( Concrete Block ( Brick ( Cement ( Wood ( Other ___________________ (tick all that apply) |
| Toilet type ( Plastic squatting slab ( Wooden squatting slab ( Concrete sanplat ( Ceramic pour flush slab ( Non-reinforced dome concrete slab ( Urine diverting toilet ( Ceramic cistern flush toilet ( Bucket latrine ( Non-flush pedestal type toilet ( Oil drum latrine ( Storage tank latrine ( Plastic bag latrine ( Portable toilet ( Trench latrine ( Defecation field ( Other ____________ |
| Privacy structure / toilet problems |
| Broken privacy structure? Toilet block unsanitary (faeces visible on toilet surface, or inside facilities)? Toilet block flooded? Insufficient number of toilets? Lack of privacy screen around toilet block? Lack of privacy inside toilet cubicle? Lack of security (lack of functional lock or lighting)? | Lack of dedicated cleaning equipment (buckets / mops, brushes, detergent etc.)? Lack of dedicated cleaning attendant? Insufficient water for adequate operation or anal-cleansing? Evidence of open defecation? Inadequate cleaning (< four times a day or strong smell of excreta or urine)? Inappropriate design? | Fly infestation (flies observed during assessment period)? Difficult access / usage for vulnerable groups (elderly / infirm / disabled / children)? Lack of personal protective equipment for cleaners (gloves, aprons, overalls, boots)? Lack of functional hand-washing station within 5m / 15ft of toilet? _________________________ _________________________ |
| Collection / storage system ( Offset pit ( Direct pit ( Double pit ( Raised pit ( Dehydrating vault ( Composting vault ( Septic tank ( Sewage holding tank ( Transfer station ( Biogas vault ( Other ____________ |
| Toilet capacity information ( Vault / pit capacity _______(m3) ( Used volume ____(%) |
| Excreta collection / storage problems |
| Excreta containment structure inadequately covered or sealed? Containment structure < 1.5m / 5ft of groundwater table? | Containment structure <30m from water source? Fly infestation (flies observed during the assessment period)? Excreta containment structure visibly cracked / broken / leaking / flooded? | Excreta containment structure full or overflowing? Presence of vermin or other vectors? _________________________ _________________________ |
| Excreta handling / desludging operations ( Human emptying ( Motorized emptying ( Buckets ( Vacuum pumps ( Diaphragm pumps ( Centrifugal pumps ( Other ____________ (tick all that apply) |
| Excreta desludging device specifications ( Device make ________ ( Device model ________ ( Power__________(kW) |
| Excreta handling / desludging problems |
| Excreta leakage? Direct contact between excreta and personnel? Visible traces of excreta on equipment during transportation or storage? | Desludging equipment or vehicles inadequately cleaned or disinfected (0.2% chlorine), between desludging? Inadequate disposal of desludging cleaning water? | Lack of personal protective equipment for desludging staff? Lack of on-site showers for desludging staff? ________________________ _________________________ |
| Excreta transportation information ( Sludge tankers ( Sludge carts ( Sealed drums ( Other ____________ (tick all that apply) ( Volume ______(m3) ( Type ___________ ( Emptying Frequency _______ ( Condition _______ |
| Excreta transportation problems |
| Excreta transportation tank overflowing, leaking, or poorly sealed / covered? Unauthorized dumping? | Visible traces of excreta on transportation system? Visible traces of excreta along transportation route? | Fly infestation (flies observed during assessment period)? Insufficient fuel / capacity? _________________________ |
| Presence and use of sewers ( Conventional sewer ( Simplified sewer ( Interceptor sewer ( Vacuum sewer ( Other ____________ ( Sewer pipe material _______ ( Sewer lengths ______(m) ( Sewer diameters ______(mm) |
| Sewer related problems |
| Sewer pipes or inspection chambers overflowing, blocked or leaking? Insufficient retention times? | Sewer pipes exposed or buried less than 0.5m / 2ft? Inspection chambers or rodding eyes inadequately sealed? | Fly infestation (one or more flies observed on inspection)? _________________________ _________________________ |
| Excreta treatment practice ( Off site sewage treatment works ( Waste stabilization ponds ( Anaerobic digester ( Constructed wetlands / reed beds ( Septic tank ( Trickling filter ( Activated sludge ( Thickening ponds ( Drying beds ( Composting ( Other ____________ (tick all that apply) ( Width ____(m) Height ____(m) Length ____(m) ( Volume ____(m3) ( Flow rate ____(l/s) |
| Excreta treatment related problems |
| Excreta containment structures cracked, broken, overflowing, leaking, flooded, inadequately covered or sealed? Insufficient retention times? | Inadequate protection from surface water? Poor maintenance schedule / lack of cleaning / replacement? Inadequate fencing? | Lack of personal protective equipment for workers? _________________________ _________________________ |
| Excreta final disposal practice ( Fill And Cover ( Leach Field ( Other __________ (tick all that apply) |
| Excreta final disposal problems |
| Untreated disposal of excreta into water bodies? Excreta disposal location less than 1.5m / 5ft above groundwater level? | Fly infestation (flies observed during the assessment period)? Application of untreated excreta to directly to land, or inadequate soil cover depth? | Lack of personal protective equipment? ________________________ ________________________ _________________________ |
| Toilet programme operation and maintenance information ( No. of toilet attendants ______ ( No. of maintenance crew ______ ( Cleaning stocks ______(weeks) ( # Shovels _____ ( # Wheelbarrows ____ ( # Buckets _____ ( # Brushes _____ ( # Mops _____ ( # Backpack sprayers ____ ( # Overalls ____ ( # Thick soled boots _____ ( # Thick gloves ____ ( # Aprons ___ ( # Eye protection ____ ( # Masks ____ ( # Chlorine ____(kg) ( Detergent ____(l) |
| Operation and maintenance related problems |
| Insufficient cleaning and maintenance staff? Staff insufficiently trained? Lack of maintenance equipment? | Poor routine cleaning and maintenance schedule? Lack of personal protective equipment? | Lack of consumables? Lack of on-site showers for sanitation workers? _________________________ |