## Slide 1: Kakuma Nutrition Survey November 2012
Training Day 4

## Slide 2: Today’s schedule
Team logistics
Equipment list
Review of sampling procedure
Obtaining consent
Practical field exercise
  Sampling, defining a household, using the even calender
Practical session in classroom
  Anthropometry
  Hemoglobin
Preparation for standardisation test next day

## Slide 3: Team logistics
Where will we meet every morning?
What equipment will you need?

## Slide 4: Equipment list
Scales
Scale carry bag/case
Spare batteries for scales
Height boards
Hemocues
Spare batteries for hemocues
Safety lancets
Microcuvettes
Tissue paper
Alcohol
Gloves
Waste bags for biohazards
Wooden board to stabilise scale on ground
MUAC tapes
Note books for survey
Pencils
Backpack or similar for equipment
Clipboard
Height screening sticks
Examples of (in small ziplock bags)
  Vitamin A pill
  Deworming tablet
  Iron/ folic acid tablet
  CSB++ empty sachet
  Plumpy’Nut and Plumpy’Sup empty sachets

## Slide 5: Review of sampling procedure
Two stage cluster sampling
  X blocks are preselected as clusters
  Within each block, X households will be randomly selected by survey team on the day of data collection
Sampling
  EPI method
  Path method
  Household list

## Slide 6: Obtaining consent – don’t forget!
Inform block leader when team arrives in block.
Introduce yourself and the survey team.
Clearly explain objectives of the survey
  What the information will be used for
  Anonymous and confidential
  The assistance the family gets will not be affected by responses
  Length of questionnaire 30m-45min
Obtain permission from the head of the household for the measurements and interviews.
Household and each individual should be able to decline if wanted.
After completion, thank all parties for their time and assistance.
Answer any additional questions.

## Slide 7: Example consent form

## Slide 8: Practical sessions
Anthropometry

## Slide 9: Practical sessions
Measuring Haemoglobin

## Slide 10: Haemoglobin – sticking a finger (1)
Prepare workstation: put on a new pair of gloves and layout all the supplies to be used for the measurement on a piece of paper roll. Close the microcuvette container immediately after taking out the microcuvette. Do not leave the microcuvette out of the container for longer than five minutes
Ensure correct position of subject: face the patient and, if you are right-handed, position yourself to be able to comfortably hold the subject’s finger with your left hand while using your right hand to hold the lancet or microcuvette (reverse if you are left-handed). A young child who is tested should be seated in the mother’s or other adult caregiver’s lap, and be provided with reassurance and distracted during testing.
Hold subject’s hand: do not hold the subject’s hand so tightly so as to obstruct blood flow.
Select finger: choose the subject’s middle or ring finger for the finger stick. The selected finger should not be callused or swollen. Remove any rings that are on this finger because the ring might interfere with blood flow. Rings on other fingers do not have to be removed unless they are in the way of the tester.
Check finger: feel the subject’s fingers for warmth. If the fingers are cold, rub the fingers vigorously or wrap them in a warm towel. If warm water is available, you can also warm them by washing them in the warm water.

## Slide 11: Haemoglobin – sticking a finger (2)
Massage finger: hold the subject’s finger for the finger stick. Use a rolling motion to gently massage the finger from the top of knuckle towards the finger tip to increase blood flow.
Disinfect finger: clean the subject’s fingertip with an antiseptic alcohol swab and allow to air dry.
Hold finger: hold the subject’s finger and apply gentle pressure to firm the skin so that the lancet will go deeper into the finger.
Place lancet: hold the lancet between two fingers and rest the thumb on the needle trigger. Place the lancet on the side of the fingertip rather than on the pad of the fingertip.
Stick finger: use a rolling motion to massage the subject’s finger even more from the top of knuckle towards the finger tip to increase blood flow. Push the lancet against the subject’s skin before triggering the needle with your thumb. Dispose of the lancet immediately after use in a biohazard waste container.
Initiate blood flow: apply gentle pressure to the wrist, palm and top of knuckle to initiate blood flow. Do not squeeze or rub the tip of the finger because you may dilute the blood drop with interstitial fluid.

## Slide 12: Filling the microcuvette
Wipe away 1st and 2nd blood drop: using a clean dry gauze pad or tissue paper, wipe away the first two drops of blood. Do not wipe away the drops with alcohol.
Sample 3rd drop: sample the third drop of blood. The drop of blood should be large enough to fill the microcuvette in one touch.
Fill microcuvette: hold the finger in one hand. Touch the tip of the microcuvette into the middle of the blood drop and fill the microcuvette completely with a single drop of blood in one step. The microcuvette fills itself by capillary action.
Inspect microcuvette: inspect the microcuvette for air bubbles and check if it is completely filled by holding it up to the light. If you see air bubbles, discard the microcuvette. If you see that it is not completely filled, discard the microcuvette. Never refill a partially filled microcuvette with the same drop of blood because the blood may have started to clot and will give an incorrect reading. If a new microcuvette is needed, refill a new microcuvette from a new blood drop from the same finger puncture if feasible. Otherwise, you may have to make a new prick. If you do need to make another prick, you should use another finger.
Wipe off excess blood: carefully wipe off any excess blood from the flat sides of the microcuvette with a clean dry gauze pad or tissue paper. Make sure that no blood is sucked out of the microcuvette while wiping it.
Place microcuvette in holder: immediately place the filled microcuvette into the microcuvette holder and read the microcuvette within three minutes of sampling.